## Slide 2
aceee.org @ACEEEdc
Non-profit research organization
Founded in 1980
80 staff and US $13 million/year budget
Act as a catalyst to advance energy efficiency policies, programs, technologies, investments, & behaviors
Funding comes from foundations, government agencies, contracts, conferences and corporate memberships

## Slide 3: ACEEE analyzed ten potential residential utility programs with large peak demand impacts
Energy efficiency programs
Electric furnace replacement program (with Energy Star heat pumps)
Attic insulation and duct sealing incentive program
Smart thermostat incentive program
Heat pump water heaters incentive program
Package of low-income programs
Monitoring-based commissioning
Small business program
Demand response programs
Central air conditioner demand response program (with smart thermostat control)
Electric vehicle managed charging program
Water heater demand response program

## Slide 4: Cumulative annual energy and peak savings by year from the programs analyzed
Chart: MW (for peak), GWh (for energy)
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Annual GWh Saved | 999.9711 | 2647.897 | 4778.3785 | 7399.7061 | 10058.3973 | 12449.596 | 14339.0804
Summer Peak MW Savings | 2744.3304 | 4792.6275 | 7119.7639 | 9593.7703 | 11917.4513 | 13549.171 | 14994.0059
Winter Peak MW Savings | 2520.4603 | 5495.9948 | 9239.3777 | 13580.8017 | 17801.3245 | 21648.1364 | 25269.1287

## Slide 5: Summer peak load reductions: 14,994 MW in 2030
Chart: MW
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Attic insulation/sealing and duct sealing | 95.3439 | 286.0318 | 572.0635 | 953.4392 | 1334.8149 | 1716.1906 | 1906.8785
Replace electric furnaces with Energy Star HP | 3.8949 | 11.6848 | 23.3697 | 38.9495 | 54.5293 | 70.109 | 85.6888
Smart thermostats | 135.4665 | 338.6662 | 541.8659 | 745.0656 | 948.2654 | 1151.4651 | 1354.6648
Heat pump water heaters | 3.9647 | 13.8764 | 31.7174 | 59.4701 | 99.1168 | 152.6399 | 222.0217
Monitoring-based commissioning | 44.4402 | 86.3447 | 128.6505 | 171.175 | 213.9306 | 256.9176 | 300.1369
Small C&I | 45.771 | 135.2735 | 266.571 | 483.9705 | 691.1278 | 888.5567 | 1076.7453
Low income | 96.0589 | 128.7703 | 286.0289 | 445.7138 | 607.8757 | 739.5631 | 869.3741
Central AC/electric heat demand response | 1329.3895 | 1994.0843 | 2658.779 | 3323.4738 | 3988.1685 | 3988.1685 | 3988.1685
Water heater demand response | 115.9667 | 231.9334 | 461.524 | 573.9766 | 685.2578 | 795.3676 | 904.306
EV charging demand response | 874.034 | 1565.9622 | 2149.1939 | 2798.5361 | 3294.3645 | 3790.1929 | 4286.0212

## Slide 6: Winter peak load reductions: 23,500 MW in 2030
Chart: MW
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Attic insulation/sealing and duct sealing | 121.7645 | 365.2936 | 730.5872 | 1217.6453 | 1704.7034 | 2191.7615 | 2435.2906
Replace electric furnaces with Energy Star HP | 461.5541 | 1384.6622 | 2769.3245 | 4615.5408 | 6461.7571 | 8307.9734 | 10154.1898
Smart thermostats | 302.9064 | 757.266 | 1211.6257 | 1665.9853 | 2120.3449 | 2574.7046 | 3029.0642
Heat pump water heaters | 6.8481 | 23.9683 | 54.7846 | 102.7211 | 171.2018 | 263.6508 | 383.4921
Monitoring-based commissioning | 18.5086 | 35.961 | 53.5807 | 71.2914 | 89.0983 | 107.0016 | 125.0017
Small C&I | 30.514 | 90.1823 | 177.714 | 322.647 | 460.7519 | 592.3711 | 717.8302
Low income | 67.5251 | 245.0116 | 531.9678 | 839.3461 | 1166.9888 | 1350.7295 | 1532.315
Water heater demand response | 144.9584 | 289.9167 | 576.905 | 717.4707 | 856.5722 | 994.2095 | 1130.3825
EV charging demand response | 874.034 | 1565.9622 | 2149.1939 | 2798.5361 | 3294.3645 | 3790.1929 | 4286.0212

## Slide 7: Utility Expenditures
Chart: Million USD
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Attic insulation/sealing and duct sealing | 267.17 | 496.1729 | 549.6069 | 732.8092 | 549.6069 | 549.6069 | 274.8034
Replace electric furnaces with Energy Star HP | 21.5367 | 43.0734 | 64.6101 | 86.1468 | 86.1468 | 86.1468 | 86.1468
Smart thermostats | 27.6462 | 41.4693 | 41.4693 | 41.4693 | 41.4693 | 41.4693 | 41.4693
Heat pump water heaters | 5.3889 | 7.506 | 9.2382 | 11.5477 | 13.8572 | 16.1668 | 18.4763
Monitoring-based commissioning | 30.4518 | 30.6175 | 30.6325 | 30.655 | 30.685 | 30.7225 | 30.7675
Small C&I | 33.3515 | 66.8845 | 100.5997 | 168.1223 | 168.5797 | 169.0384 | 169.4983
Low income | 73.7388 | 192.0679 | 314.1646 | 319.1913 | 324.2983 | 312.0717 | 317.0649
Central AC/electric heat demand response | 150.0488 | 122.1684 | 145.7403 | 169.3123 | 192.8843 | 141.4319 | 141.4319
Water heater demand response | 18.1143 | 28.3056 | 55.5823 | 57.6557 | 67.1376 | 76.5222 | 85.8093
EV charging demand response | 33.9347 | 64.7766 | 90.4294 | 87.1942 | 103.5492 | 68.0767 | 76.9824
7 year total – $8.8 billion

## Slide 8: Benefit-Cost Ratios
Chart: Efficiency (green) and demand-response (gray) measures
| Heat pump water heaters | Smart thermostats | Replace electric furnaces with Energy Star HP | Monitoring-based commissioning | EV charging demand response | All Efficiency | Small C&I | Attic insulation/sealing and duct sealing | All Energy Efficiency and Demand Response | All Demand Response | Central AC demand response | Low income | Water heater demand response
 | 9.4404 | 8.7574 | 6.7238 | 4.5585 | 4.454 | 2.9475 | 2.9321 | 2.71 | 2.4115 | 2.2132 | 1.7821 | 1.4064 | 0.91334
B/C = 2.9 for full package

## Slide 9: Comparison of Full and Alternate Scenarios
Chart: MW
| Summer peak MW savings in 2030 (full scenario) | Summer peak MW savings in 2030 (alternative scenario) | Winter peak MW savings in 2030 (full scenario) | Winter peak MW savings in 2030 (alternative scenario)
Attic insulation/sealing and duct sealing | 1906.8785 | 953.4392 | 2435.2906 | 1217.6453
Replace electric furnaces with Energy Star HP | 85.6888 | 85.6888 | 10154.1898 | 10154.1898
Smart thermostats | 1354.6648 | 1354.6648 | 3029.0642 | 3029.0642
Heat pump water heaters | 222.0217 | 222.0217 | 383.4921 | 383.4921
Monitoring-based commissioning | 300.1369 | 300.1369 | 125.0017 | 125.0017
Small C&I | 1076.7453 | 0 | 717.8302 | 0
Low income | 869.3741 | 434.6871 | 1532.315 | 766.1575
Central AC/electric heat demand response | 3988.1685 | 3988.1685 | 1475.5415 | 1475.5415
Water heater demand response | 904.306 | 0 | 1130.3825 | 0
EV charging demand response | 4286.0212 | 4286.0212 | 4286.0212 | 4286.0212
Chart: Millions USD per year
| Average annual expenditure (full scenario) | Average annual expenditure (alternative scenario)
Attic insulation/sealing and duct sealing | 488.5394 | 244.2697
Replace electric furnaces with Energy Star HP | 43.0734 | 43.0734
Smart thermostats | 39.4946 | 39.4946
Heat pump water heaters | 11.7402 | 11.7402
Monitoring-based commissioning | 30.6474 | 30.6474
Small C&I | 125.1535 | 0
Low income | 259.4356 | 129.7178
Central AC/electric heat demand response | 151.8597 | 151.8597
Water heater demand response | 55.5895 | 0
EV charging demand response | 54.2691 | 54.2691

## Slide 10: Alternative Scenario (8 programs, 78-85% of the peak reductions, 56% of the costs
Program | Customers served | Peak savings in 2030 (MW) |  | Energy savings (GWh) | Costs ($million)
 |  | Summer | Winter |  | 
Efficiency |  |  |  |  | 
Replace electric furnaces with Energy Star HP | 602,933 | 86 | 10,154 | 1,281 | 302
Heat pump water heaters | 299,385 | 222 | 383 | 636 | 82
Attic insulation/sealing and duct sealing (half) | 1,090,490 | 953 | 1,218 | 2,496 | 1,710
Smart thermostats | 2,764,622 | 1,355 | 3,029 | 2,488 | 276
Monitoring-based commissioning | 735 | 300 | 125 | 1,315 | 215
Low-income (half) | 1,112,456 | 435 | 766 | 1,006 | 908
Subtotal | 5,870,621 | 3,351 | 15,676 | 9,222 | 3,493
Demand Response |  |  |  |  | 
Central AC/electric heat demand response | 2,611,032 | 3,988 | 1,476 |  | 1,063
EV charging demand response | 750,000 | 4,286 | 4,286 |  | 380
Subtotal | 3,361,032 | 8,274 | 5,762 |  | 1,443
TOTAL | 9,231,653 | 11,625 | 21,437 | 9,222 | $4,936
Scaled-back as % of full |  | 78% | 85% | 60% | 56%
Add 13.75% reserve margin |  | 13,223 | 24,385 |  | 
Annual average (without reserve margin) |  | 1,661 | 3,062 | 1,317 | $705

## Slide 11: Energy Savings Targets (MWh) as % of Sales for States with Efficiency Targets
Chart: 
| New York | Rhode Island | Illinois | Colorado | Maryland | Vermont | New Jersey | California | Hawaii | Minnesota | Oregon | Arkansas | Virginia | U.S. Average | Massachusetts | Nevada | Arizona | Maine | Michigan | New Mexico | Iowa | Washington | Connecticut | Wisconsin | District of Columbia | Pennsylvania | Texas | U.S. Average
Approx. annual electric savings target | 0.02 | 0.019 | 0.018 | 0.017 | 0.017 | 0.016 | 0.016 | 0.015 | 0.014 | 0.013 | 0.013 | 0.012 | 0.012 | 0.012 | 0.011 | 0.011 | 0.011 | 0.01 | 0.01 | 0.01 | 0.009 | 0.009 | 0.007 | 0.007 | 0.007 | 0.006 | 0.002

## Slide 12: Comparison of Current Participation to ACEEE Recommendations
Note: 2022 info from draft TetraTech report
 |  | ACEEE Recommendations | 
Program | 2022 | 2024 | 7-year average
Heat pump to replace elec. furnaces | 22 MW | 462 MW | 1450 MW
Attic insulation and sealing | Well established; participation not provided | 109,000 homes | 312,000 homes
Heat pump water heaters | 71 units | 17,000 units | 43,000 units
Smart thermostats | Installed over 9000 units | 276,000 units | 395,000 units
Low income programs | $25.6 million in spending in 2021 | $74 million in spending | $265 million in spending
Small business | 6 dedicated programs, participation not provided | 3300 buildings | 12,000 buildings
Monitoring-based commissioning | 4 programs + custom applications; participation not provided | 122 million sq. ft. of building floor area | 122 million sq. ft. of building floor area
Central AC DR | 3 programs reducing load 72 MW; infrastructure in place to ramp-up if needed | 1329 MW of load reductions | 3988 MW of load reductions in 2030
Water heating DR | Current M&V can handle | 278,000 homes | 2.2 million homes in 2030
EV DR | 19 chargers in 2022; one study in 2023 | 153,000 homes | 750,000 homes in 2030

## Slide 13: Conclusions
Energy efficiency and demand response can and should be critical resources for Texas, helping to reduce peaks:
  15,000 MW summer peak
  23,500 MW winter peak
This can be done with an average benefit-cost ratio of 2.9
  $20/month in benefits per customer at average cost of $7/month
Texas has good programs but these are underfunded and need to be expanded

## Slide 14
Contact Information
Steven Nadel
snadel@aceee.org