## Slide 1: Energy Efficiency Implementation Project (EEIP) Meeting
Austin, Texas
October 12, 2021

## Slide 2
VALUES
Team—we employ exceptional people and foster a culture of collaboration and safety across our enterprise
Relationships—we forge strong personal connections with our clients to deliver the solutions that best fit their needs
Integrity—we conduct business in a transparent manner and deliver precise, comprehensive, and unbiased information
Planet—we are committed to environmental stewardship
PY2022 TRM 9.0
Summary of Key Measure Updates

## Slide 3
Peak Methodology:
  Claimed peak savings for sites with multiple energy efficiency projects with independent operation are allowed to utilize different peak seasons:
  Example:
    HVAC retrofit with new building automation controls must claim savings for using the same peak period because they operate as a system
      Note: This also applies when using a combination of deemed savings and measurement and verification (M&V).
    Lighting retrofit with interior and exterior fixtures may use both summer and winter demand seasons because exterior fixtures they operate independently.
Vol 1 Overview

## Slide 4
Peak Methodology (Continued):
  Peak Probability Analysis (PPA) tables include TMY3 temperatures. Direct readers to Texas Efficiency website for access to TMY3 data files, including other data points eligible for use in custom regressions.
Texas Efficiency Website:
  Climate zone mapping
  EUL summary spreadsheet
  Lighting Survey Form (LSF) Fixture Codes – also referred to as Standard Wattage Table
  Reminder: RES HVAC tables are also available in spreadsheet form
Vol 1 Overview

## Slide 5
Estimated Useful Life (EUL):
  Verify measure life values referencing Database of Energy Efficiency Resources (DEER) reports against new DEER Remote Ex-Ante Database Interface (READI) tool.
Remaining Useful Life (RUL):
  Systems that were manufactured after current standard/code are not eligible to use early retirement baseline.
  Increment tables for compliance with minimum age requirement.
  Ineligible RUL values are preserved for use when standards are updated.
Vol 2-3 General Measure Life Review

## Slide 6
2.1 Lighting:
  Existing methodology is also applicable to LED fixtures with integrated LEDs using equivalent wattage as applicable baseline.
  Update midstream guidance for compliance with EM&V memo (same as TRM 7.0).
Vol 2 Residential

## Slide 7
2.2 HVAC:
  2.2.3 GSHPs: Unit correction on heating energy savings algorithm.
  2.2.4 Central AC/HPs:
    Systems with non-compliant EER are still eligible to claim energy and winter demand savings. Summer demand savings ineligible.
    Heating savings are awarded based on AHRI rated cooling capacity. Deemed savings calculation already account for difference between rated cooling and heating capacities.
  2.2.5 Mini-Split AC/HPs: Same as previous measure.
Vol 2 Residential

## Slide 8
2.2 HVAC:
  2.2.6 Large Capacity AC/HPs: Add GSHP coincidence factors.
  2.2.8 Room ACs: Add efficiency condition for units with connected functionality, as these units have a lower minimum efficiency requirement than standard RACs.
    Units with connected functionality (tested for demand response capabilities) receive a 5% credit toward ENERGY STAR certification.
    Add efficiency condition for units with connected functionality (5% over federal standard vs. 10% for standard units).
  2.2.9 Connected Thermostats: Advise against use of emergency heat setting for thermostats installed on HPs. Supplemental heat is already available in freezing conditions using normal settings.
Vol 2 Residential

## Slide 9
2.3 Envelope:
  2.3.2 Ceiling Insulation:
    Add < R5 baseline category to encourage targeting of homes with lower baseline R-values. Original photo requirements still apply.
    New baseline is compliant with previous EM&V guidance restricting baseline R-value to R-5+.
  2.3.3 Attic Encapsulation: Same as previous measure.
  2.3.7 Low-E Storm Windows: New measure targeting glazing attachments with low-emissivity coating added to existing windows.
  2.3.9 Cool Roofs: New < R5 baseline pending EM&V review.
Vol 2 Residential

## Slide 10
2.4 DHW:
  2.4.6 HPWHs: Clarify use of ROB baseline for ER projects. No separate ER baseline available at this time.
  2.4.8 Showerhead TSRVs: Restrict measure eligibility to homes with electric DHW.
  2.4.9 Tub Spout & Showerhead TSRVs: Same as previous measure.
Vol 2 Residential

## Slide 11
2.5 Appliances:
  2.5.2 Clothes Washers: Update deemed savings to match current ENERG STAR appliance calculator methodology and assumptions.
    Add < R5 baseline category to encourage targeting of homes with lower baseline R-values. Original photo requirements still apply.
    New baseline is compliant with previous EM&V guidance restricting baseline R-value to R-5+.
  2.5.7 Pool Pumps: Unit correction on energy savings algorithm.
  2.5.9 Advanced Power Strips: Confirm and document derivation of coincidence factors, resulting in minor updates to winter values.
  2.3.9 Cool Roofs: New < R5 baseline pending EM&V review.
Vol 2 Residential

## Slide 12
2.1 Lighting:
  2.1.1 Lamps and Fixtures:
    Formalize standard wattage table and make available on Texas Efficiency website.
    Provide QPL guidance for delisted products, model numbers with slight variances, and fixtures made available in various lengths. Refer to EM&V guidance memo for parent/child products while DLC QPL is being updated.
    Correct lumen ranges for outdoor athletic new construction baseline
    Provide citations for peak demand factor development
Vol 3 Non-Residential
Notes: Previous methodology for reflector lamps came from ENERGY STAR Lamp Center Beam Intensity Benchmark Tool.

## Slide 13
2.1 Lighting:
  2.1.1 Lamps and Fixtures (continued):
    Update midstream guidance for compliance with EM&V memo:
      Use TRM 7.0 as starting point.
      Require use of QPL equivalent wattage as baseline for all lamp types in lieu of specifying a separate methodology* for reflector lamps, eliminating need for rounding guidance.
      Consolidate < 100 W lamp type categories into GSL and reflector.
      Update outdoor hours to match TRM 8.0 update to AOH table.
  2.1.1 Lighting Controls: Restrict new construction control savings enforce code requirements. Allow savings for control types exceeding code.
* Previous methodology refers to ENERGY STAR Lamp Center Beam Intensity Benchmark Tool
Vol 3 Non-Residential
Notes: Previous methodology for reflector lamps came from ENERGY STAR Lamp Center Beam Intensity Benchmark Tool.

## Slide 14
2.2 HVAC:
  2.2.2 Split & Packaged AC/HPs:
    Assume “All Other” heating section type for ACs. HPs already assume “Electric Resistance or None”.
    For AC to HP conversions, use HP heating savings coefficients as baseline proxy.
    Incorporate midstream methodology from 2020 EM&V guidance memo.
    Set default age equal to EUL, consistent with Volume 2.
  2.2.3 HVAC Chillers: Same as previous measure for midstream and EUL guidance.
  2.2.4 PTACs, PTHPs, and RACs: Same EUL guidance and unit correction for winter peak savings algorithm.
Vol 3 Non-Residential

## Slide 15
2.2 HVAC:
  2.2.5 CRACs: Add capacity conversion from kW to Btu/hr.
  2.2.7 HVAC VFDs: Update building type operating schedules and expand list of available building types.
  2.2.8 Evaporative Pre-Cooling: Reinforce that savings algorithms use units of tons for capacity and kW/ton for efficiency. Add conversions from other unit types.
  2.2.10 Small Commercial Evaporative Cooling: New measure targeting installation of evaporative coolers in small commercial and converted residence applications. Savings account for offset energy consumption from preventing installation of refrigerated cooling.
Vol 3 Non-Residential

## Slide 16
2.3 Envelope:
  2.3.2 Window Treatments: Update baseline solar heat gain coefficients (SHGC) values to complete transition from shading coefficients (SC) to SHGC.
2.4 Food Service
  All ENERGY STAR measures:
    Update savings algorithms, input assumptions, and deemed savings for compliance with 7/15 amendment to March 2021 update to ENERGY STAR commercial food service calculator.
    Update terminology and documentation requirements for consistency across measures.
Vol 3 Non-Residential

## Slide 17
2.4 Food Service:
  2.4.1 Combination Ovens: Correct idle rate formulas to match ENERGY STAR specification.
  2.4.9: Pre-Rinse Spray Valves:
    Update savings algorithms and ensure proper citations for all input assumptions.
    Update peak demand coefficients for compliance with current peak definition.
Vol 3 Non-Residential

## Slide 18
2.5 Refrigeration:
  All measures:
    Update savings algorithms and ensure proper citations for all input assumptions.
    Update for compliance with current peak definition and climate zones.
  2.5.7 Strip Curtains: Complete measure redesign. Replaced savings derived from M&V study with methodology aligning with other food service measure updates. Vary savings by building type.
  2.5.8 Zero-Energy Doors: Clarify savings units (per door rather than per linear feet).
Vol 3 Non-Residential

## Slide 19
2.6 DHW:
  New section made up of existing measures.
  2.6.2 Showerhead TSRVs: Restrict measure eligibility to homes with electric DHW.
  2.6.3 Tub Spout & Showerhead TSRVs: Same as previous measure.
Vol 3 Non-Residential

## Slide 20
2.7 Miscellaneous:
  2.7.1: Vending Machine Controls: General text edits to clarify eligibility criteria, baseline and efficiency conditions, and measure documentation requirements.
  2.7.4 Pool Pumps: Correct turnovers/day savings inputs; savings not affected.
  2.7.5 Computer Power Management: Update peak demand coefficients for compliance with current peak definition. Eliminated winter demand, which is already associated with hours of inactivity.
  2.7.7 Electric Vehicle Supply Equipment: Eliminate documentation requirements related to vehicle type and estimated miles driven per day.
Vol 3 Non-Residential

## Slide 21
2.7 Miscellaneous:
  2.7.8 VFDs for Water Pumping: New measure targeting installation of VFDs for water pumping (e.g., domestic water supply, wastewater treatment, and conveyance).
  2.7.9 Steam Trap Repair/Replacement: New measure targeting steam trap repair, including the installation of Venturi steam traps. VSTs continuously remove condensate via water pressure rather than using moving parts.
  2.7.10 Hydraulic Gear Lubricants: New measure targeting improvement of gear efficiency (1% per gear mesh) by reducing friction with lubricants.
  2.7.11 Hydraulic Oils: New measure similar to previous measure targeting friction reduction for moving parts in gearless applications. Efficiency improvement = 3.2%.
  New measures will target underserved manufacturing and industrial customers.
Vol 3 Non-Residential

## Slide 22
2.1.2 – GSHPs
  Increase EUL from 15 to 20 years to match Volume 2 GSHP measure.
2.2.1 – Residential New Construction
  Add HVAC commissioning and dehumidification system to reference home definition.
2.3.1 – Residential Solar PV; 2.3.2 – Non-Residential Solar PV
  Update PVWatts software modeling instructions, examples, and documentation requirements.
2.3.3 – Solar Shingles
  Establish 20-year where none was previous specified.
2.3.4 – Solar Attic Fans
  Reinstate measure removed from TRM 8.0 requiring M&V data collection.
Vol 4 M&V protocols

## Slide 23
Vol 4 M&V protocols
2.4.1 – Behavioral; 2.4.3 – Non-Residential RCx
  Update model requirements to account for pandemic and other non-routine events.
2.5.1 – Residential Load Management
  Define peak demand period and add links to utility program manuals.
2.5.2 – Non-Residential Load Management
  Exclude eligibility of critical load customers without backup generation.
  Replace utility program details tables with links to program manuals.

## Slide 24
Derek Neumann, Frontier Energy
dneumann@frontierenergy.com
737.236.0298