## Slide 1
Water Loss: Status Update
October 11, 2017
Dan Strub, Conservation Program Coordinator

## Slide 2
The Infrastructure Leakage Index decreased from 3.88 in 2015 to 3.31 in 2016
Program history and calculation methods available in attached primer
Water Loss Trend

## Slide 3
Two transmission main leaks discovered & repaired
Total number of leaks roughly constant
Average time to repair leaks remaining below 2 days
  Response time is less
  High priority leaks get addressed more quickly
What’s Going On

## Slide 4
Metering
  AMI
  Large Meter Testing
  Large Meter Replacements
  Small Meter Replacements
  Small Meter Accuracy Study
District Metered Areas
Renew Austin
Leak Detection
Current Efforts
Notes: Replaced 10 fire demand meters in FY17 - (4) 6”, (5) 8” and (1) 10”
Renewing Austin Program goal is 52000 LF of main replacement a year. Completed 56,297 LF in 2016. So far, in FY17 it has completed 32,597 LF and expected to replace 55000 LF

## Slide 5
In-House
Distribution mains
  Wachs and ADS
Transmission mains
  PURE
  Piloting 2 competitors in FY18
Year | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Miles | 869 | 698 | 720 | 433 | 322 | 710
Year | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Miles | 7.59 | 9.08 | 5.68 | 6.32 | 8.9 | 11.1
Current Leak Detection Efforts

## Slide 6
4 New FTEs in FY17
  2 for small meter replacement
  2 for leak detection
Utilis/Hydromax
Echoshore-M
Mueller/Echologics
PICA/Aganova and MTA-Messtechnik
New Water Loss Efforts
Notes: Leak detection FTEs also have new leak detectors and correlators. They surveyed 54 miles so far in 2017.

## Slide 7
Satellite-based sensing
Pilot for 3 sets of images
First images processed and leaks identified; 30% success rate on sites investigated
Second images are processed and on-the-ground follow-up pending
Utilis/Hydromax Leak Detection

## Slide 8
Transmission main leak detection
Non-invasive
Identifies and correlates
Potentially much more economical
Began using in April
Echoshore-M
Notes: Attached to appurtenances on 16 to 90 inch mains, transmit data cellularly
Surveyed 2.6 miles so far

## Slide 9
In Brentwood/N Lamar neighborhood
Sensors permanently installed on hydrants
Piloting in conjunction with meters to test AMI network
Installed 33 hydrant sensors and 20 AMI meters in May/June
Mueller/Echologics leak detection
Notes: Detects and correlates, sends daily reports, good for up to 5 years

## Slide 10
AMI – Consultant Selection (November)
Leak Detection/Condition Assessment contract renewal (November)
Future WWW Actions